_______________

|  | INTERNATIONAL TELECOMMUNICATION UNION |
| --- | --- |

CCITT	G.707

THE  INTERNATIONAL
TELEGRAPH  AND  TELEPHONE
CONSULTATIVE  COMMITTEE

GENERAL  ASPECTS  OF  DIGITAL

TRANSMISSION  SYSTEMS;

TERMINAL  EQUIPMENTS

SYNCHRONOUS  DIGITAL  HIERARCHY
BIT  RATES

Recommendation  G.707

|  | Geneva, 1991 |
| --- | --- |

Printed in Switzerland

FOREWORD

The CCITT (the International Telegraph and Telephone Consultative Committee) is a permanent organ of the International Telecommunication Union (ITU). CCITT is responsible for studying technical, operating and tariff questions and issuing Recommendations on them with a view to standardizing telecommunications on a worldwide basis.

The Plenary Assembly of CCITT which meets every four years, establishes the topics for study and approves Recommendations prepared by its Study Groups. The approval of Recommendations by the members of CCITT between Plenary Assemblies is covered by the procedure laid down in CCITT Resolution No. 2 (Melbourne, 1988).

Recommendation G.707 was prepared by Study Group XVIII and was approved under the Resolution No. 2 procedure on the 5 of April 1991.

___________________

CCITT  NOTES

1)	In this Recommendation, the expression “Administration” is used for conciseness to indicate both a telecommunication Administration and a recognized private operating agency.

2)	A list of abbreviations used in this Recommendation can be found in Annex A.

ã  ITU  1991

All rights reserved. No part of this publication may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm, without permission in writing from the ITU.

PAGE BLANCHE

Recommendation G.707

Recommendation G.707

SYNCHRONOUS  DIGITAL  HIERARCHY  BIT  RATES

(Melbourne 1988, revised 1990)

The CCITT,

considering

(a)	that Recommendation G.702 specifies a number of digital hierarchy bit rates for 1544 kbit/s and 2048 kbit/s based digital networks;

(b)	that the various hierarchy levels specified in Recommendation G.702 are interconnected by means of digital multiplexing employing justification methods;

(c)	that synchronous digital multiplexing and a related synchronous digital hierarchy offer advantages such as:

–	simplified multiplexing/demultiplexing techniques;

–	direct access to lower speed tributaries, without need to multiplex/demultiplex the entire high speed signal;

–	enhanced operations administration and maintenance (OAM) capabilities;

–	easy growth to higher bit rates in step with evolution of transmission technology;

(d)	that the synchronous digital hierarchy rates need to be chosen such that they allow the transport of digital signals:

–	at hierarchical bit rates as specified in Recommendation G.702;

–	at broadband channel bit rates;

(e)	that Recommendation G.708 specifies the network node interface (NNI) for the synchronous digital hierarchy;

(f)	that Recommendation G.709 specifies the synchronous multiplexing structure;

(g)	that Recommendations G.707, G.708, and G.709 form a coherent set of specifications for the synchronous digital hierarchy and network node interface (NNI),

recommends

(1)	that the first level of the synchronous digital hierarchy shall be 155 520 kbit/s;

(2)	that higher synchronous digital hierarchy bit rates shall be obtained as integer multiples of the first level bit rate;

(3)	that higher synchronous digital hierarchy levels should be denoted by the corresponding multiplication factor of the first level rate;

(4)	that the following bit rates should constitute the synchronous digital hierarchy.

TABLE  1/G.707

| Synchronous digital hierarchy level | Hierarchical bit rate kbit/s |
| --- | --- |
| 1 | 155 520 |
| 4 | 622 080 |
| 16 | 2 488 320 |

Note – The specification of levels higher than 16 requires further study.

ANNEX

(to Recommendation G.707)

Alphabetical list of abbreviations used
in this Recommendation

NNI		Network-node interface

OAM		Operations, administration and maintenance

SDH		Synchronous digital hierarchy